## Slide 1: CUDA Optimization Techniques
Anfal AlYousufi
Department of Computer science and engineering
University of South Florida
July 16th 2018
aalyousufi@mail.usf.edu

## Slide 2: Outline
Terms of optimization:
  Optimizations for latency bound kernels
  Optimization for compute bound kernels
  Optimization for memory bound kernels

## Slide 3: Optimizations for latency bound kernels

## Slide 4: Optimizations for latency bound kernels
Processor stalls/idle: cannot execute the next instruction due to a dependency on the previous instruction.
Stall waiting on a[i] from memory
Time(clocks)

## Slide 5: Hiding latency in gpu
GPUs:
  Minimize the impacts of stalls
  by interleaving execution of
  many threads on a single core.
Data-parallel model:
  Can always execute threads
  from different blocks independently.
  Can execute threads within a block
  independently.
  * unless constrained by

## Slide 6: CUDA THREAD HIERARCHY
A kernel is executed over a thread
hierarchy:
i) Threads are grouped into
thread blocks
ii) Threads blocks are grouped
into a grid

## Slide 7: The cuda programming model
Blocks from the multithreaded/grid being distributed across streaming multiprocessor(SMs)
Each block will only execute one multiprocessor.
  But, multiprocessor could execute multiple blocks.
  Blocks must be independent

## Slide 8: What is a warp?
The SM creates, schedules, manages and executes thread in the group of parallel threads called warps.
Individual threads composing a warp start together at the same program address but are otherwise free to branch and execute independently.
When a multiprocessor is given one or more thread blocks to execute, it splits them into warps that get scheduled by the SM.
Warp: a group of 32 threads that gets allocated or divided from the block.
  Example: launching a block with 96 threads would be portioned to up to 3 warps of 32 threads each.

## Slide 9: Resources allocation
When a block is scheduled to run on a multiprocessor, resources in that SM are allocated on an exclusive basis:
  Shared memory-per block
  Register-per block, with unique registers for each thread with the block.
This enables zero-overhead switching between warps at any point in their execution.

## Slide 10: WARP execution
A scheduler on a SM evaluates all available warps to find on that is ready to execute an instruction
  Eg. Not waiting on data from memory
The instruction is executed for the warp
The scheduler re-evaluates all available warps instruction
The effectively hides latency if:
  There is a high ratio between arithmetic and memory operations/synchronization
  OR there are enough warps to select from
Instructions for a warp are still executed in order!

## Slide 11: occupancy
Occupancy= active warps / maximum active warps multiprocessor
Occupancy determined by:
  Choice of block size
  Kernel register usage
  Shared memory usage
  Hardware limitations
Limitations | Compute 2.x | Compute 3.x | Compute 5.0 | Compute 5.2 | 
Max no. of thread/block | 1024 | 1024 | 1024 | 1024 | 
Warp size(no. of threads) | 32 | 32 | 32 | 32 | 
#Registers/SM (KB) | 32768 | 65536 | 65536 | 65536 | 
Shared memory/SM (KB) | 16/48 | 16/32/48 | 64 | 96 | 
Max no active blocks/SM | 8 | 16 | 32 | 32 | 
Max no active warps/SM | 48 | 64 | 64 | 64 | 
Max no. active threads/SM | 1536 | 2048 | 2048 | 2048 | 

## Slide 12: Occupancy and performance
Switching to other warps to mask latency is key to performance!
  Need ‘enough’ other work to mask
    May not need 100% occupancy!
    Once you have reached the threshold, additional occupancy won’t improve performance.
  ‘Enough’ occupancy depends on the code
    Memory bound kernels typically need more then compute bound
Often trading off resource usage for occupancy
  May change algorithmic efficiency too!

## Slide 13: Occupancy examples

## Slide 14: Occupancy examples

## Slide 15: Optimizing latency bound kernels
Low theoretical occupancy
  Adjust block size, register usage, shared memory usage.
  Occupancy calculator can help!
Low achieved occupancy
  Eg. Launching 32 blocks of a kernel that runs with 2 blocks/SM on a GPU with 16 SMs.
    Theoretical occupancy is 100%
    Achieved occupancy is approx. 50%
  Consider concurrent kernel execution

## Slide 16: Optimizations for compute bound kernels

## Slide 17: Efficiency and branching
GPU executes instruction for the entire warp.
Full efficiency is realized when all 32 threads of a warp agree on their execution path.
If thread of a warp diverge via a conditional branch, the warp serially executes each branch path
  Only the active threads in the warp execute the instructions for a path. Threads from the warp on other paths are idle.
  Hence, hardware is underutilized when this occurs
  Branch divergence occurs only within a war!

## Slide 18: Efficiency and branching

## Slide 19: Iteration/loop unrolling (cont)
For small loop bodies reduce the loop overhead by unrolling
For known trip counts the compiler will unroll the loop
  Ensure trip count is known at complete time by templating the kernel
Control unrolling with #pragma unroll
  #pragma unroll 1 prevents unrolling
  #pragma unroll N unrolls the loop N times
  #pragma untoll unrolls the loop completely

## Slide 20: ‘Fast’ math
Consider intrinsic function
  Approximate versions of many math library functions
  Slightly reduced accuracy, higher throughput
  __sinf() vs sinf()
Compiler flags
  --use_fast_math : redirect all math functions to intrinsic
  -prec-div=false
  -prec-sqrt=false

## Slide 21: Intrinsic benchmarks

## Slide 22: Shuffle instruction on Kepler
Allows threads within a warp to share data
  Use this functionality instead of shared memory
  A single shuffle instruction can replace shared memory write/sunc/read sequence
Any thread can read any other thread’s data within a warp
  __shfl()
Support for useful patterns
  __shfl_up()
  __shfl_down()
  __shfl_xor()

## Slide 23: Optimizations for memory bound kernels

## Slide 24: Memory access patterns
Simple task:
  Traverse and increment contiguous 2D memory
  (stored as row-major)

## Slide 25: CUDA MEMORY SPACES (REVIEW)
Several memory “spaces”
  Programmer-controlled hierarchy
  Spaces vary by:
    Size
    Location(on/off chip)
    Scope
    Cached/non
    Access(R/W)
    Performance rules
    Latency/thoughput

## Slide 26: GLOBAL MEMORY
Global memory is most efficient when threads in a warp access an aligned contiguous region of memory
  Individual thread requests can be combined (or coalesced) into fewer and larger transactions.
Can be quite inefficient otherwise
  Minimum transaction size across the bus
  For Kepler GPUs, minimum transaction size is a 32B aligned L2 cache line
Specifics depend on GPU architecture, word size (1,2,4,8 byte words), and access patterns

## Slide 27: ACCESS PATTERN EXAMPLES(1)
Maximized the amount of memory that you are going to be able to bring it across the bus

## Slide 28: Access pattern examples (2)
Request 128B
16x32B loads
25% efficiency

## Slide 29: ACCESS PATTERN EXAMPLES (3)

## Slide 30: ACCESS PATTERN EXAMPLES (4)

## Slide 31: SUMMARY LATENCY LIMITED KERNELS
Low theoretical occupancy
  Adjust block size, register usage, shared memory usage.
  Occupancy calculator can help!
Low achieved occupancy
  Consider concurrent kernel execution
    Theoretical occupancy is 100%
    Achieved occupancy is approx. 50%
  Eg. Launching 32 blocks of a kernel that runs with 2 blocks/SM on a GPU with 16 SMs.

## Slide 32: SUMMARY COMPUTE BOUND KERNELS
Branching/warp divergence
Loop unrolling
Fast math
Shuffle

## Slide 33: SUMMARY MEMORY BOUND KERNELS
Global Memory
  Access patterns
  Data structures
Shared Memory
  Bank conflicts
  64-bit accesses
Constant memory vs Read-only cache

## Slide 34: Work cited
Paper`1: Extending parallelization of the self-organizing map by combining data and network partitioned methods by Richardson, Trevor & Winer, Eliot
Paper`2: Computation of gray-level co-occurrence matrix based on CUDA and its optimization by Hong, Huichao & Zheng, Lixin & Pan, Shuwan
Paper’3: A CUDA-Based Real Parameter Optimization Benchmark by Ding, Ke & Tan, Ying
Chapter 6 “PERFORMANCE CONSIDERATIONS” : Book: Programming Massively Parallel Processor By David & Wen-mei
Chapter 8 “APPLICATION CASE STUDY: ADVANCED MRI RECONSTRUCTION” : Book: Programming Massively Parallel Processor By David & Wen-mei
Chapter 12 “2 CONCLUSION AND FUTURE OUTLOOK” : Book: Programming Massively Parallel Processor By David & Wen-mei
Youtube: CUDA Part D: GPU Optimization Part 2; Peter Messmer (NVIDIA)